## Slide 1: Advanced PlayStation Audio ‘98
Libspu optimizations
Introduction to libmidi

## Slide 2: libspu - Volume Modes
SPU master volume and voice volume
    Range -0x4000 to 0x3fff
CD input
    Range -0x8000 to 0x7fff
Direct volume mode
  Volume is set to input parameter
  Negative volumes allow for 3D Sound
    X360

## Slide 3: libspu - Volume Modes
Exponential & linear volume modes
  Increase
  Decrease
  Normal phase
  Reverse phase (for negative volumes)
  Ramps from current level to 0 or maximum volume in hardware

## Slide 4: libspu - Volume Modes
Exponential & linear volume modes
  Parameter determines ramp speed
    0 is instantaneous (or nearly so)
    Below ~0x28, an inverse value is added per tick
    ~0x3f increases the volume 4-7 points per 16 ticks
    >~0x3f, the same volume increase takes more ticks
    0x7f is infinite (or nearly so)
  Verify correct mode-sign combination

## Slide 5: libspu - Volume Modes
Exponential & linear volume modes
  SpuGetVoiceVolume() returns input parameters
  SpuGetVoiceVolumeX() returns actual volume
    Scales volumes from -0x8000 to 0x7fff
  Can stop an effect very near a desired point
    Set a timer
    SpuGetVoiceVolume(voice, &voll, &volr )
    SpuSetVoiceVolumeAttr(voice, voll>>1, volr>>1, SPU_VOICE_DIRECT, SPU_VOICE_DIRECT)

## Slide 6: libspu - Voice Allocation Tips
Methods of testing voice status
  SpuGetKeyStatus()
  SpuGetAllKeysStatus()
  SpuRGetAllKeysStatus()
Components of voice status
  Software key on/off
  Envelope playback

## Slide 7: libspu - Voice Allocation Tips
Voice status
  SPU_ON
    Keyed on, voice actively playing
  SPU_OFF
    Keyed off in software, voice finished playing
  SPU_ON_ENV_OFF
    Keyed on, voice not yet playing OR
    Keyed on, one shot VAG expired
  SPU_OFF_ENV_ON
    Keyed off in software, release state entered

## Slide 8: libspu - Voice Allocation Tips
Possible problems
  SPU_ON_ENV_OFF state ambiguous
  SPU registers only flushed every 1/44,000 second
  Wasted cycles occur if voice status checked every allocation
Solution - create a new voice status check and voice allocation scheme

## Slide 9: libspu - Voice Allocation Tips
Set in key on/off functions
  Voice on/off flag (vo_flag)
    Tracks software key on/off
  Newly keyed on flag (nko_flag)
    Flags voice for first frame of key on
  Looping voice flag (lp_flag)
    Sound data structure must include loop info

## Slide 10: libspu - Voice Allocation Tips
Set once per frame (or less)
  Voice free flag (vf_flag)
    Is the voice allocable?
  Envelope on/off flag (env_flag)
    Is the voice playing data?
  One-shot expiry flag (exp_flag)
    Has one-shot voice naturally expired?
    nko_flag and exp_flag combine to resolve SPU_ON_ENV_OFF ambiguity

## Slide 11: libspu - Voice Allocation Tips
Once per frame (or less often)
  Push key on/off queue
  Skip lp_flag low & nko_flag low voices
  Check envelope state
    Fill env_flag using SpuGetVoiceEnvelope()
  If env_flag low & vo_flag high
    Set exp_flag high OR
    If exp_flag already high
      Clear exp_flag & Clear vo_flag
  Determine vf_flag with env_flag & vo_flag
  Clear nko_flag & exp_flag

## Slide 12: libspu - Keying Sounds On/Off
Problems
  Key on/off commands may be missed
    Key on/off queue contains high bits for voices which must be keyed on or off
    Old queue is flushed out
    SPU registers only read every 1/44,000 second
  Cycles wasted
    Voices reallocated before playback begins
Solution - queue ALL key on/off commands

## Slide 13: libspu - Keying Sounds On/Off
Create two additional 24-bit variables
  keyoff_flag& keyon_flag
In key on function
  Bit OR keyon_flag & clear keyoff_flag bit
  Bit OR nko_flag
  Bit OR lp_flag if looping sound
  Do NOT call SpuSetKey()

## Slide 14: libspu - Keying Sounds On/Off
In key off function
  Bit OR keyoff_flag & clear keyon_flag bit
  Clear nko_flag bit for that voice
  Clear lp_flag bit for that voice
  Do NOT call SpuSetKey()
Once per frame, before voice status check
  SpuSetKey(SPU_ON, keyon_flag)
  SpuSetKey(SPU_OFF, keyoff_flag)

## Slide 15: libmidi - Increased Functionality
Channel-level pitch bend changes
  Notes may be bent INTO
RPN data
  RPN 0 (pitch bend max and min setting)
  RPN 1 (tone shift changes)
  RPN 2 (tone center changes)
Damper changes on a channel level, rather than a global level
Reset all controllers supported

## Slide 16: libmidi - Increased Functionality
Song level pan shift/time effect
  Similar to a crescendo/ decrescendo
Voice level note shift/time effect
  Doppler type effect
Current tempo of songs retrievable
Cancellation of transfer to SPU RAM
  SsVabTransBodyPartly() does not support this
Vibrato
Portamento

## Slide 17: libmidi - Increased Functionality
Nested song loops
Current tempo retrievable
Cancellation of time-based effects
  Reports back the amount of effect and time remaining
  Volume, pan, tempo (song level only), pitch (voice level only)

## Slide 18: libmidi - New File Formats
MAB
  Reduced structure sizes
    VabHdr level
    ProgAtr level
    VagAtr level
    Vag Offset Table
    Unused tone slots not stored
MEQ
  Loop marker & callback marker messages reduced to one message
  File size reduced and MIDI time conserved

## Slide 19: libmidi - Linkable Functions
SPU RAM management
  Use libspu standard SPU RAM management functions OR
  Create smaller or “best-fit” functions OR
  Hardcode all transfers to minimize code size
Pitch calculation
  Use library standard function OR
  Create larger PLU table for more precision or smaller PLU table for less code size

## Slide 20: libmidi - Linkable Functions
Volume calculation
  Least complex
    Requested level volume and pan
  Medium complexity
    Requested and tone level of volume and pan
    Exponential left/right separation of song voices
  Most complex
    Requested, tone, program, and bank levels of volume and pan
    Exponential left/right separation of song voices

## Slide 21: libmidi - Linkable Functions
Voice allocation
  First available voice & priority-based system
  Addition of envelope size & age
Low-level MIDI functions

## Slide 22: More libmidi
Reduced structure sizes
    Song management table
    Voice management
Reduced tick callback cycle usage
    Not wrapped around libspu calls
    Data transfer to SPU registers only if necessary
    Fewer I-cache misses at tick callback
Standardization
  Key on commands take volume and pan
    Easier to pan voices
  Seq/Sep duality removed - extra wrapper

## Slide 23: libmidi - Tools
Initially
  seq2meq
  VAB2MAB
Coming
  smf2meq
  MABmaker