## Slide 1
PDA Preview
Thomas Daniel,
SCEE Technology Group

## Slide 2: Overview
Introducing the PDA
  Description and applications
Technical description
  CPU, memory, other features
Software development
  Hardware and software tools
Miscellaneous details
  Support, licensing and launch

## Slide 3: What is the PDA?
A new platform, and a new peripheral
  Software supplied as part of a PlayStation title
Same size as a Memory card
  Backwards compatible with Memory cards
Additional features
  Programmable CPU
  LCD display
  Infra-red communications
  Real-time clock
Notes: The bottom part of the PDA with the buttons flips up to reveal a connector for a Memory card slot

## Slide 4: Possible PDA applications
Memory card
Virtual pet
  Pet characters from games
Pocket watch / calendar / phone book
  “Free” with games
Multi-purpose remote control unit
Edit game saves and exchange data
  Portable garage
  Player management
Notes: These applications might form part of the game or somehow enhance the game.
“Free” PDA programs with a game or demo can be used as marketing aids

## Slide 5: Hardware features (1)
LCD display
  32x32 pixels, monochrome
  Programmable refresh rate - 16/32/64Hz
Buzzer
  10-bit DAC
5 buttons
  4 directional buttons + 1 “fire” button
  All buttons can interrupt the CPU
Notes: The display is quite small - probably only 8 by 8 characters will be visible. Artwork will have to be “creative”.
Scrolling and virtual screens could be used, SRAM permitting. These are not supported in hardware though. There is only a memory-mapped display buffer.
By reducing the refresh rate of the screen, the power consumption is reduced, leading to longer battery life.
Buzzer - be very careful with memory space - don’t try to store long sound samples. Best to create waveforms on-the-fly.

## Slide 6: Hardware features (2)
Integral battery
  Disposable button cell
  Power saving must be done in software - be sensible
Real-time clock
  Can interrupt CPU once per second
  3 16-bit countdown timers can also interrupt
Notes: Battery life is precious.
Use power saving techniques involving the LCD refresh, CPU speed and (if applicable) IR transceiver.
Clock can obviously be used for a calendar and stuff. Go idle between interrupts to save power.

## Slide 7: Hardware features (3)
Infra-red communications
  Transceiver built in to every PDA
  IrDA capable
  Will possibly also produce a carrier-based signal (TV remote etc)
  Can be used when the PDA is a standalone device or when attached to a PlayStation
Notes: The main purpose of the IR is PDA to PDA communications. Since the IR still works when the PDA is attached to the PlayStation, it can be used as a communication device for the PlayStation.
IrDA - communicate with PCs and other digital devices
Carrier - communicate with other devices such as TVs and stereos. This is still under evaluation and may not make it into the final product.

## Slide 8: PDA CPU
ARM7TDMI-based
  32-bit RISC CPU
  Clock speed programmable from 32KHz to 4MHz
  2 instruction sets, ARM and Thumb
  128K Flash RAM, 2K SRAM, 16K ROM
  Interruptible by button pushes or real-time clock
  Memory Management Unit
Notes: ARM are your friends.
The clock speed can actually go up to 8MHz but since memory accesses take 2 cycles in this mode the effective maximum speed is 4MHz
MMU is very good because of the way the OSD loads (or rather doesn’t) load PDA executables into the address space - no extra RAM is required for temporarily storing the program since the MMU arranges for the Flash RAM to be mapped directly into the CPU address space.

## Slide 9: ARM instruction set
Full 32-bit mode
13 general purpose registers plus PC, LR and SP, second bank of 15 for privileged mode
Conditional execution on all instructions
  Optionally update condition flags
Rich instruction set
  Multiplier with optional accumulate
  Shifts free with many operations (MOV/ADD etc)
  Multiple register load/store instructions
Notes: The addressing modes and shifter may make ARM code denser and more efficient than Thumb (see next page)

## Slide 10: Thumb instruction set
16-bit instruction word, 32-bit registers
Code typically 35% smaller than ARM code
8 general-purpose registers + PC, LR and SP
  Map to ARM registers 0 to 7
  8 “High” registers for MOV,ADD and CMP
Same basic instructions as ARM, but
  Separate shift instructions
  Conditional execution only on branches
  Condition flags always updated
Notes: Code density is important to save space in the Flash RAM.
Thumbinstruction execution time is nearly always the same as ARM because Thumb instructions are internally mapped to ARM instructions. However, ARM instructions can do more processing per intruction.
Swap instruction sets on the fly using the BX instruction. Branch & Xchange instruction takes 3 cycles to execute
Data must be aligned in Thumb mode

## Slide 11: ARM vs Thumb (1)
ARM code
LDR r0,=array_base
LDR r2,[r0,r1,LSL #2]
8 bytes
Result in 6 cycles
Thumb code
LDR r0,=array_base
LSL r2,r1,#2
LDR r2,[r0,r2]
6 bytes
Result in 6 cycles
Accessing 32-bit wide array elements (index in r1)
Notes: = means literal from the literal pool, generated by the assembler.
The extra LSL instruction in the Thumb code is pipelined with the previous LDR
Little bits of execution time is not hugely important because the CPU is so powerful. Unless of course you can optimise it so much that you can reduce the clock speed.

## Slide 12: ARM vs Thumb (2)
ARM code
ADDEQ r0,r0,LSL #2
4 bytes
Result in 1 cycles
Thumb code
BNE done
LSL r1,r0,#2
ADD r0,r1
6 bytes
Result in 5 cycles
Uses 1 extra register!
Multiplying r0 by 5 if previous comparison was equal
Notes: Demonstrates both the lack of free shifts and the lack of conditional execution in Thumb mode

## Slide 13: PDA memory
16K ROM
  Actually Flash, but not for general use
  Contains kernel, boot code & OSD
  Kernel controls memory card functionality
128K Flash RAM
  Contains game saves and PDA executables
  8K blocks mapped to address space by MMU
2K SRAM
  Usable by executing programs
Notes: The OSD has a startup menu so that the user can choose from a set of programs loaded onto the PDA.
Memory card functionality will operate independently of the PDA application execution.
Flash RAM contains the game saves and can be mapped into the address space in 8K blocks (The same size as a Memory card block). PDA apps appear as Memory card saves to maintain compatibility with existing software on the PlayStation side. To make your program take fewer blocks, use Thumb mode. Code in assembler if possible to try to reduce code size.
SRAM is very small. Remember that the Flash RAM is mapped into the address space so blocks which have been allocated to the program can be used although it may be slow.

## Slide 14: Developing PDA applications
Development hardware supplied by SCEE
Tool chains already available
  ARM Software Development Toolkit
  GNU tools - to be supported by SN Systems
Additional tools provided by SCEE
  Specifications of low-level Memory card format
  Specifications of PDA hardware, but no libraries
  New Memory card library for PlayStation
Notes: There will be an additional license fee for the ARM STD. A 30-day evaluation version of the ARM STD may be available on the next SCEE developers’ CD-ROM.

## Slide 15: PDA Hardware tools
DEX-4000
  Standalone development box
  Contains all PDA hardware
Multi-ICE
  Plugs in to PC and DEX-4000
  Offers in-circuit debugging facilities
Notes: An ICE (In-Circuit Emulator) is a device which emulates a CPU. Externally it appears to the hardware as a normal CPU but to the user it is a very powerful tool because you can use it to get cycle-by-cycle information about what it going on. You can use hardware breakpoints for debugging and have access to all memory and registers.

## Slide 16: SDevTC development environment
Pro-DG IDE
32-bit GNU tools
  Separate compilers for ARM and Thumb
SDevTC Windows debugger
  To offer full PDA support
Real-time PDA emulation
Notes: The SDevTC PDA emulator is currently an R&D project and may not be released.

## Slide 17: ARM development environment
IDE
  Project manager
  Editor
C compiler and assembler
  Can produce both ARM and Thumb code
Debugger
  Powerful source and object-level debugger
  ARMulator

## Slide 18: Getting support
Supported the same way as PlayStation
  Developer Support hotline and e-mail
  Developers’ web site
PDA newsgroups
  Recommended point of contact for developers
  Monitored by support engineers, other developers and SN Systems

## Slide 19: Software licensing
All licensed PlayStation developers can develop PDA applications
  SDevTC and ARM tools supplied by SCEE
  License fee for DEX-4000 and Multi-ICE to be confirmed
No additional software royalties
  Software will be seen as enhancements for PlayStation titles rather than new products
Notes: The QA procedure for titles using the PDA is yet to be decided.

## Slide 20: PDA launch details
Retail price under £30
Launch in Japan for Christmas 1998
SCEE/SCEA territories’ dates to be confirmed
  Possible SCEE territories launch Q2 1999
  First hardware tools available Q3 (or Q4) 1998
Specification identical worldwide

## Slide 21: PDA Questions?
scee.dev.programming.pda
Dev_Support@Playstation.sony.com
Or ask me now