## Slide 1: H2700 Masterclass
Making the most of the PlayStation
(with a little help from the PA)

## Slide 2: Overview
Basic H2700 Use
CPU optimisations
GPU optimisations
Debugging using the PA

## Slide 3: Basic H2700 use
The H2700 consists of 2 parts
  A standard playstation devkit
  A logic analyser ( Performance Analyser )
The PA part helps you to fine tune your games

## Slide 4: Using the PA
The PA monitors 3 buses
  Main Bus
  Sub Bus
  Video Bus
It only knows about bus activity
Notes: The H2700 performance analyser grabs data consisting of the following blocks
Main bus address lines
Main bus control lines
Main bus data lines
Sub bus address lines
Sub bus control lines
Video bus address lines
Video bus control lines
Because no data lines are captured for the sub bus, and more importantly for the video bus, you cannot see what pixel data is being used by the GPU. However the software does show frequency of access, which is more useful for showing texture misses etc. ( although not as pretty to look at )

## Slide 5: Using the PA
The PA operates independantly of the devkit
A snapshot of the bus activity is taken
  The PA can hold approx 7 Vsyncs of data
This data is then analysed by the PA software
  PA software interprets raw data to show PS structures
Notes: As well as the 8M of ram for the devkit, the H2700 has a further 64M of ram for the PA functionality. This memory is filled up at the bus clock rate (33MHz) allowing the analysis of the system in fine detail, at the expense of continual real time monitoring, which is best performed with the debugger.
The PA software interprets the data intelligently, further analysing bus activity to show up DMA activities ( and even GPU packet types )
Future versions of the PA software will allow the user to analyse the data themselves.. ( via DLL and drivers )

## Slide 6: Using the PA
Make a scan
  Use trigger function to isolate problems
Identify bottlenecks.
  CPU or GPU speed problems
Change code
Repeat ad nauseum

## Slide 7: CPU optimisation
I-cache optimisation
Data optimisation

## Slide 8: I-cache optimisation
Avoid cache thrashing between routines
Reduce size of core loops
Notes: The I cache is direct mapped, so it is very easy to have two routines that share the same cache lines. ( Basically the bottom 12 bits of the address represent the cache address ) If you see a repeating pattern of I-cache reads when you zoom in on a scan then this is usually caused by two routines thrashing the cache. If possible changing the position of one of your routines in your source code can fix the problem, but in most cases using inline functions or macros is better.
The other cause of slowdowns due to cache refilling is where you have large loops that don’t fit onto the cache. In this case the start and end points of the loop clash. Normally the only way to fix this is to rewrite your code with the aim of reducing the size. Also separating complex loops into a series of simpler loops helps, as each loop then fits completely on cache.
I cache reads are very fast, taking 4 cycles to read the first long, then 1 cycle per long for the rest of the cache line. This is followed by a precharge cycle ( which occurs for all memory accesses ) The R3300 supports instruction streaming which allows the CPU to execute instructions as soon as they are available, rather than waiting for the entire cache line to be read from memory.

## Slide 9: Data optimisation
Main memory is slow
Use scratchpad ram for locals
  Using stack on scratchpad is good
Always try to group memory accesses into longs
  Quicker to pack / unpack in registers
Notes: A main memory read on the playstation requires 4 cycles for the access, with 1 cycle to precharge the DRAM ready for the next access. There is also a variable number of internal cycles ( from 1 to 3 ) needed internally because of writeback and possible pipeline stalls. For data reads there is no page mechanism, all reads take the same number of cycles.
A main memory write takes 3 cycles to set up, 2 cycles to perform the write, and 1 cycle to precharge. However the CPU can speed up writes to the same page. ( See page 13 )

## Slide 10: Slow code example
loop:
lb v0,(a0)
add a0,a0,1
sb v0,(a1)
add a1,a1,1
bne a0,a2,loop
nop

## Slide 11: Optimised code example
lw t0,(a0)
lw t1,4(a0)
lw t2,8(a0)
lw t3,12(a0
sw t0,(a1)
sw t1,4(a1)
sw t2,8(a1)
sw t3,12(a1)

## Slide 12: Main bus reads
R3300 has load scheduling
  CPU doesn’t stall while waiting for bus.
Only 1 read can be pending
You can only interleave 5 instructions
  2 cycles are eaten
Notes: Normally a data read from DRAM takes 6 cycles, and a load instruction will stall for that time. If you place your loads sequentially then each load will take 6 cycles. ( This is the quickest way to read memory as the bus cycles are back to back )
The R3300 has a R buffer to support load scheduling, which lets the CPU continue executing without waiting for the load to complete. However when loads are not consecutive there are 2 internal stall cycles ( bringing the total read time up to 8 cycles ) You can interleave up to 5 instructions between the loads, but you can’t recover the 2 stall cycles.
If you alternate loads and stores with no instructions between there is only a single stall cycle.
You can interleave most instructions ( including GTE ops and GTE transfers , but not GTE memory accesses ) between loads without overheads. But a taken branch does stall until the memory access is complete ( This may be because of the bus snooping mechanism on the CPU )

## Slide 13: Bus writes
PS has 4 write buffers
  Up to 4 writes can occur before bus activity
Writes to same page are quicker
You can group more than 4 writes in one burst
Notes: If the bus is busy when a write occurs the value is placed into 1 of 4 write buffers and the CPU continues execution. This means that up to 4 writes can be pending before any stall cycles occur. However a write will occur as soon as the bus is busy, or if any read occurs ( even a read to scratchpad ram )
One nice point about the data write mechanism is that it supports fast page access. If more than one value is written to the same page the timings will be 3 cycles setup + 2 cycles per write + 1 cycle precharge for next access. You can group as many writes as possible together. ( which is useful for fast copying to main ram )
You can also interleave instructions between writes, but in most cases you wont need to because of the multiple write buffers.

## Slide 14: Scratchpad
The scratchpad isn’t on the bus
However it is in memory
  Scratchpad load will stall any uncompleted read

## Slide 15: GTE
GTE memory accesses are same as R3300
GTE register moves can be interleaved

## Slide 16: DMA
GPU dma is fast ( Single cycle )
SPU dma is slower
CD dma is very slow
All dma operations reduce bus time available to CPU
Bus is allocated on a round robin basis.

## Slide 17: Common GPU optimisations.
Texture cache optimisations
CLUT thrashing
Primitive combinations
Clipping

## Slide 18: Debugging using the PA
GPU Timeouts
Catching strange problems
Reflashing the H2700 rom
Notes: A GPU timeout occurs when the GPU has remained inactive for a long period of time. This is almost always due to an inconsistency between the DMA size ( found in the packet header ) and the size expected by the executing GPU command. To trace these trigger a scan based on the timeout message with a capture window containing at least 6 vblanks before the trigger point. You can then find the last DMA packet sent to the GPU to determine what has gone wrong.
Other problems can occur on certain debug stations, and not be repeatable using the devkit. These are normally due to either corruption of kernel ram by rogue pointers, or interference between the OSD (on screen display ) program found in the ROM. However by using the flash utility supplied with the PA and a relevant rom image it is possible to grab data whilst a gold disc or image is booting ( The program PSXCONS is useful with this as it allows you to change the memory configuration, boot with EPROM or flash and check CD contents as seen by the PS rather than the PC ) By setting the trigger point around the area you think is causing the problem you can see where memory accesses are going awry.

## Slide 19: Summary
CPU efficiency is becoming more important for PS games
In most cases CPU time is greater than GPU time
Speed can be increased by working with rather than against the PS design

## Slide 20: Questions??